## Slide 1: Geospatial Data Acquisition Model

## Slide 2: Components
Resource Discovery
Data Profiling
Cleansing and Standardization
Merge and Fill
Validation
Data Ingestion

## Slide 3: Resource Discovery
Source | Cost | Update | Standard | Format
Open Street Map | - | Once per Year | All ESPG | Road LineString SHP
Humdata | - | Once per 3 Years | ESPG 32618 | Road LineString SHP
… |  |  |  | 

## Slide 4: Data Profiling
Source | # Records | Attributes | Completeness | Set As Master
Open Street Map | 153,759 | osmid, geometry, name, highway, length, oneway, etc | 51% | Y
Humdata | 78,095 | cod_tronc, cod_urbain, cod_route, nom_sec, nom_off | 45% | N
… |  |  |  | 

## Slide 5: Data Profiling
Attribute | Type | Completeness
osmid | Unique ID | 8.2%
name | Road name | 0.6%
highway | Highway ID | 0.7%
oneway | Oneway flag | 0.0%
length | Segment length | 0.0%
geometry | LineString | 100%
Attribute | Type | Completeness
cod_tronc | Unique ID | 5.7%
cod_route | Road code | 0.4%
cod_urbain |  | 0.0%
nom_off | Road name | 0.9%
nom_sec | Segment Name | 0.7%
geometry | LineString | 100%
OPEN STREET MAP
HUMDATA

## Slide 6: Cleansing & Standardization
Apply projection standard EPSG 4326
Apply standard missing value as NULL
Generate unique identifier for analysis
Rename attributes contain the same measurement
…

## Slide 7: Merge
Explode geometry to points
Apply K Nearest Neighbors to match similar points
Transfer attributes from points to points
For each attribute, vote the most frequent value from points as the value of the geometry.
Aggregate points back to geometry

## Slide 8: Merge – Geometry Explode
Before
ID | Geometry | Road Name
osm-1298 | ([lat,lon], [lat,lon], …) | NULL
osm-241 | ([lat,lon], [lat,lon], …) | xxx
After
ID | Geometry | Point ID | Point | Road Name
osm-1298 | ([lat,lon],..) | osm-1298-1 | [lat1, lon1] | NULL
osm-1298 | ([lat,lon],..) | osm-1298-2 | [lat2, lon2] | NULL
osm-1298 | ([lat,lon],..) | osm-1298-3 | [lat3, lon3] | NULL
osm-241 | ([lat,lon],..) | osm-241-1 | [lat4, lon4] | xxx
osm-241 | ([lat,lon],..) | osm-241-2 | [lat5, lon5] | xxx

## Slide 9: Merge – KNN Matching
Point ID | ID | Road Name | Point ID Matched | ID Matched | Road Name Matched | Distance | Validate
osm-241-1 | osm-241 | xxx | hum-2059-1 | hum-2059 | NULL | 0.000109 | Y
osm-241-2 | osm-241 | xxx | hum-2059-3 | hum-2059 | NULL | 0.000031 | Y
osm-1298-1 | osm-1298 | NULL | hum-4211-7 | hum-4211 | www | 0.000389 | Y
osm-1298-2 | osm-1298 | NULL | hum-5892-1 | hum-5892 | yyy | 0.000180 | Y
osm-1298-3 | osm-1298 | NULL | hum-5892-3 | hum-5892 | yyy | 0.000076 | Y
osm-1298-4 | osm-1298 | NULL | hum-9087-1 | hum-9087 | zzz | 0.019021 | N
NULL | NULL | NULL | hum-9087-2 | hum-9087 | zzz | 0.000201 | Y
NULL | NULL | NULL | hum-9087-3 | hum-9087 | zzz | 0.000054 | Y

## Slide 10: Merge – Transfer Attributes
Point ID | ID | Road Name | Point ID Matched | ID Matched | Road Name Matched | Distance | Validate
osm-241-1 | osm-241 | xxx | hum-2059-1 | hum-2059 | NULL | 0.000109 | Y
osm-241-2 | osm-241 | xxx | hum-2059-3 | hum-2059 | NULL | 0.000031 | Y
osm-1298-1 | osm-1298 | www | hum-4211-7 | hum-4211 | www | 0.000389 | Y
osm-1298-2 | osm-1298 | yyy | hum-5892-1 | hum-5892 | yyy | 0.000180 | Y
osm-1298-3 | osm-1298 | yyy | hum-5892-3 | hum-5892 | yyy | 0.000076 | Y
osm-1298-4 | osm-1298 | NULL | hum-9087-1 | hum-9087 | zzz | 0.019021 | N
hum-9087-2 | hum-9087 | zzz | hum-9087-2 | hum-9087 | zzz | 0.000201 | Y
hum-9087-3 | hum-9087 | zzz | hum-9087-3 | hum-9087 | zzz | 0.000054 | Y

## Slide 11: Merge – Vote Most Frequent Attributes
Point ID | ID | Road Name | Point ID Matched | ID Matched | Road Name Matched | Distance | Validate
osm-241-1 | osm-241 | xxx | hum-2059-1 | hum-2059 | NULL | 0.000109 | Y
osm-241-2 | osm-241 | xxx | hum-2059-3 | hum-2059 | NULL | 0.000031 | Y
osm-1298-1 | osm-1298 | yyy | hum-4211-7 | hum-4211 | www | 0.000389 | Y
osm-1298-2 | osm-1298 | yyy | hum-5892-1 | hum-5892 | yyy | 0.000180 | Y
osm-1298-3 | osm-1298 | yyy | hum-5892-3 | hum-5892 | yyy | 0.000076 | Y
osm-1298-4 | osm-1298 | yyy | hum-9087-1 | hum-9087 | zzz | 0.019021 | N
hum-9087-2 | hum-9087 | zzz | hum-9087-2 | hum-9087 | zzz | 0.000201 | Y
hum-9087-3 | hum-9087 | zzz | hum-9087-3 | hum-9087 | zzz | 0.000054 | Y

## Slide 12: Merge – Aggregate Back
Before
ID | Geometry | Road Name
osm-1298 | ([lat,lon], [lat,lon], …) | NULL
osm-241 | ([lat,lon], [lat,lon], …) | xxx
After
ID | Geometry | Road Name
osm-1298 | ([lat,lon], [lat,lon], …) | yyy
osm-241 | ([lat,lon], [lat,lon], …) | xxx
hum-9087 | ([lat,lon], [lat,lon], …) | zzz

## Slide 13: Validation

## Slide 14: Data Ingestion
Ingest shape file to NGA database

## Slide 15: Geospatial Data Acquisition Infrastructure & Tools

## Slide 16: Tool Comparison
Features | ArcGIS | Mapbox | Azure Maps | GeoPandas
Cost | $$$ | $$ | $$ | Free
Profiling | ✓ | ✓ | ✕ | ✓
Standardization | ✓ | ✓ | ✓ | ✓
Merge | ✕ | ✕ | ✕ | ✓
Validation | ✓ | ✓ | ✓ | ✓
Automation | ✓ | ✓ | ✕ | ✓
Export | ✓ | ✓ | ✓ | ✓

## Slide 17: Infrastructure Comparison
Features | On-Prem | Cloud Native | Cloud Agnostic
Cost | $$$ | $$ | $
Data Volume | ✕ | ✓ | ✓
Auto-Scaling | ✕ | ✓ | ✓
Processing Speed | ✕ | ✓ | ✓
Automation | ✓ | ✓ | ✓
Maintenance | ✕ | ✓ | ✕
Security | ✓ | ✕ | ✓